## Slide 1
Lahaye Loïc
DesCar manual
Design and characterization software
DesCar
Initiative

## Slide 2
Lahaye Loïc
2
Thermal stress computation
By differential Stoney
Lahaye Loïc

## Slide 3
Lahaye Loïc
3
Lahaye Loïc
Start DesCar by running the main file DesCar.py => you’ll need to install all the required python packaged
If first boot of the software type 1 and provide a source and destination path (they can be the same).
  The paths will be saved between DesCar sessions in boot.txt
DesCar should initialize from there. Type help to list all the functions or help + a specific function

## Slide 4
Lahaye Loïc
Lahaye Loïc
Organize the clean .txt Dektak files like following (stack folders): layer_NameOfLayer_thicknessInNanoMeters. Descar’s stoney routine will use the folder name to get the thickness and stack position info => do it right !
In this case the layer 0 is the virgin substrate and the layer 1 is the thermal oxide
Careful !! Files in the folders MUST have matching names !

## Slide 5
Lahaye Loïc
Lahaye Loïc
Tell DesCar to look for folders at the root of your stack folders

## Slide 6
Lahaye Loïc
Lahaye Loïc
(Facultative) Tell DesCar to load silicon from its material library. The properties of silicon will automatically be used for the substrate by the stoney routine. You can skip this step to manually enter the parameters later
Run the stoney routine. DesCar will ask you to do what was just described. Check that all is good

## Slide 7
Lahaye Loïc
Lahaye Loïc
DesCar outputs the residual thermal stress per measurements
DesCar saves the approximation of curves for validation and outputs a text report of the results and configurations

## Slide 8
Lahaye Loïc
8
Membrane deflection
Depending on P polytec
Lahaye Loïc

## Slide 9
Lahaye Loïc
9
Lahaye Loïc
Start DesCar by running the main file DesCar.py => you’ll need to install all the required python packaged
If first boot of the software type 1 and provide a source and destination path (they can be the same).
  The paths will be saved between DesCar sessions in boot.txt
DesCar should initialize from there. Type help to list all the functions or help + a specific function

## Slide 10
Lahaye Loïc
10
Lahaye Loïc
Setting up the measurements
  Be sure that the measurement contains the pressure information.
  You do not have to mention in the file name line or map.
If you measure pressure cycles (pressure up then down) make sure that your measurement connects and save them in marked separated folder:
For better results you must do a double measurement at the end/beginning of a pressure phase.
  E.g: you measure from 0 to 10 kPa then from 10 kPa to 0
    Put the measurement from 0 to 10 in a folder named up_1
    Put the measurement from 10 to 0 in a folder down_1
    Make sure that the 10 kPa measurement is done twice => one time for the up and one time for the down
    Do the same if more cycles are needed with the same naming convention
See example =>

## Slide 11
Lahaye Loïc
11
Lahaye Loïc
Measurement setup
The 80 kPa is measured two times. This allows to eliminate any offset and connect cyclic measurement

## Slide 12
Lahaye Loïc
12
Lahaye Loïc
Run the setPlot command
Change path to your measurement folder and run the polytecDeflection command for automatic processing. Follow the instructions
  The tool will parse and clean the line and map files automatically
  You’ll be asked to level the data
  You end up with a txt file of the deflection as a function of the pressure
  Repeat the command for every measurement folder

## Slide 13
Lahaye Loïc
13
Lahaye Loïc
In the case of looped measurements: Rename the final deflection data (up1, down1, …).
Put them in a single folder
Run the polycycle command
Connected up/down measurements
Drifted measurement
Raw measurements