## Slide 1: Condor
A modeling framework for disciplined engineers with a deadline
Benjamin W. L. Margolis, PhD
Kenneth R. Lyons, PhD
Joseph A. Garcia, PhD

## Slide 2: Motivation
There are multiple programs/projects within the Agency that are interested in MDAO and 6DOF vehicle simulations.
  ARMD: 1) EPFD, 2) AATT, 3) IASP, 4) SFD
  HEOMD/NESC: Orion, HLS, etc
EPFD in particular has 3+ years of investment in a SOTA optimization framework without achieving the performance, robustness, or even flexibility of heritage tools; no delivery of promised solution to coupled optimization problem

## Slide 3: If you could start from “scratch,” what would you do?
Leverage existing computational technology from the Machine Learning (ML) and Artificial Intelligent (AI) community
  Automatic Differentiation (AD)
  Code generation/Computational acceleration
Leveraging existing best practices for library design: Application development code should be ….
    Concise
      “Expressive” coding means less typing for the developer, focus is on actual modeling
      Let the computer handle the repetitive part of writing code leading to less opportunity for human error
    Well organized
      Separation of distinct code by purpose (e.g. a model vs. numerical algorithm/tuning)
      Easier to read, write, and debug code
      Easier maintenance, only change code in a single location = DRY (don’t repeat yourself) code
Key: don’t start from scratch!

## Slide 4: Documentation-driven design
OpenMDAO
Condor
99 Lines
2,188 Characters
39 Lines
612 Characters

## Slide 5: Decide how user code should look then make it possible
OpenMDAO
Condor
99 Lines
2,188 Characters
39 Lines
612 Characters

## Slide 6: First draft
Leverage existing technology: AI/ML communities know how to efficiently solve models for gradient-based optimization.
Rapid model development in Python
Symbolic and Automatic Differentiation
Computation acceleration:
Compiled C/Fortran
GPU and distributed HPC
Automatic interfacing to well-known solvers
Facilitate interface to existing codes

## Slide 7: Goals
Use pythonic patterns, built-ins, and existing libraries as much as possible
Through Leveraging existing off-the-shelf (AI/ML) technology and best practices for code development
  Use well vetted tools that can do Automatic Differentiation (AD)
  Reduce the time to code development both to upgrade existing code and to modify it to expand it capability
  Improve robustness of the tool chain due to the above benefits
  Speed up the CPU time to solutions due to Code generation/ Computational acceleration
Delivery of analysis! Not tool development

## Slide 8: DRY organization
Condor model layer: what users write to describe model
Implementation layer: interface between condor model; generates everything needed to call numerical solver/perform numerical evaluation
solver layer: (numerical) algorithm+code for most models, e.g., Newton’s method, IPOPT, SGM
Backend: casadi
represent elements from fields (i.e., inputs, outputs) and basic expressions (“symbols”)
Represent models as “advanced” expressions (e.g., casadi.callback, aesara.op) with partial derivative definitions
propagate (symbolic) derivatives through expressions
Callable for numerical evaluation

## Slide 9: Backend
Currently using casadi because it ships with all required functionality:
  Easily represent symbolic elements, condor Models, and expressions
  Propagate derivatives through symbolic expression tree
  Generate C code for numerical evaluation of expression tree
  Provides interfaces to IPOPT solvers at the C level
Other backends (e.g., SymPy, Aesara, etc) could be used, but some of the required functionality may need to be developed
To use a new backend, new implementation layer will be required to generate callables for model (and derivatives) to pass to solvers

## Slide 10: Layer boundaries
Models use Fields generate elements (symbol atoms/leaves) for system input and build expressions for system output/internal solver computation using model-based, unary, and binary operations
Implementation for each model template provides two interfaces between the Model layer and symbolic backend:
  Generates a symbolic operator for the model so symbolic backend can propagate derivatives through model [“model-based operator”]
  Generates a numeric callable for the model so the model can be evaluated numerically; typically requires generating numerical callable for internal fields (and gradients) and passing that to the solver
  For casadi, the “callback” performs both and only requires numerical implementation and metadata – likely typical
    implementation should primarily be responsible for collecting/flattening fields
    custom callbacks should generate callables to pass to solver; casadi.callback.eval should just call solver with args – only ever sees numeric, casadi internals handle symbolic case
    solver should only interface with numeric callable
  --> Bind both symbolic and numeric results to model instance

## Slide 11: The Model layer
User Model classes inherit from a Model template
Model templates define the fields from which symbolic elements are drawn
Disciplined system encapsulation: build up more complex models by using sub-models, but only interact through input and output fields
Model class and ModelType metaclass implement “metaprogramming” (dynamic class generation) that enable the desired API
Solver options can be set using as Model inner-class namespace (or in separate code, executed before model calls) to provide clear separation between mathematical model and numerical details
 | Fields |  | 
Built-in template | input | internal | output
ExplicitSystem | input parameter? |  | output
TableLookup | input parameter?! | input_data output_data | output
AlgebraicSystem | parameter | residual | implicit_output explicit_output variable output
OptimizationProblem | parameter | objective constraint | variable output
TrajectoryAnalysis | parameter | state dot initial event.update modal control | trajectory_output output

## Slide 12: The Model layer
User Model classes inherit from a Model template
Model templates define the fields from which symbolic elements are drawn
Disciplined system encapsulation: build up more complex models by using sub-models, but only interact through input and output fields
Model class and ModelType metaclass implement “metaprogramming” (dynamic class generation) that enable the desired API
Solver options can be set using as Model inner-class namespace (or in separate code, executed before model calls) to provide clear separation between mathematical model and numerical details
 | Fields |  | 
Built-in template | input | internal | output
ExplicitSystem | input |  | output
TableLookup | input | input_data output_data | output – make free
AlgebraicSystem | parameter | residual | variable
OptimizationProblem | parameter | objective constraint | variable
TrajectoryAnalysis | parameter | state dot initial event.update modal control | trajectory_output output

## Slide 13: Model definitions are symbolic
For most mathematical models, this is what you want
Conditionals: Use float-casting of boolean expressions to construct piecewise models instead of if-else flow control
higher-level interfaces: settings module
  a module can define settings that change the model definition
  Variables that user can set must be defined in a dict [SimpleNamespace?] and passed to condor.settings.get_settings.
  To access the dynamically defined model, use
  module_ref = condor.settings.get_module(<path.to.module>, **user_settings)
  instead of
  import <path.to.module>
If you need a lot of conditionals, loops, and interface logic maybe you need a new template, implementation, and/or solver
RENAME: Grammar should be “configure model”

## Slide 14: Open questions/tasks
Rename “symbols” to “elements” where appropriate?
Change output from assigned field to free field
How to bind programmatic sub-models? Name for model instances!
Refine patterns for programmatic connections – defining sources from existing models (use dot access naming with actual object reference or with strings), grouping IO with easy looping, etc.
Helper to wrap algebraic/optimization in explicit
Leverage bound sub-models to serialize? Can just save all attributes that are bound and/or initialize solver state
Make implementation layer backend agnostic by forcing compile evaluator (callback/op),
Symbolic layer between model and backend for backend-agnostic symbolic manipulations? Maybe just need to add __op__ methods for base symbol.
Serialization? Easy save program state. It kinda just works to use numpy savez with the IO fields
Add bind_sub_model flag (back) to model meta?
Make more magic/automatic conversion between base symbols and the backend symbol class?

## Slide 15: Future work with more developers
MPI-compiled backend/solver
Template for prototyping high performance CFD – like pymbolics guy
Graphical/web front end
Alternate backends (e.g., aesara)
Compilation/performance optimization
TOOL WRAPPERS (with AD)
  SOCP interface
Make sure default is parallelizable for e.g., monte carlo
Linter configuration to make condor code pass :)

## Slide 16: Performance Considerations for Trajectory
Moved to scikits.odes CVODE, an implicit solver; implicit may generally be slower but more accurate than explicit? but faster per accuracy? see discussion://github.com/bmcage/odes/issues/127#issuecomment-923782240.
May be able to use state ordering so banded jacobian can be used. Other solver configuration options may improve performance as well.
Implicit means iterative solution at every time step  solvers (AlgebraicSystem or OptimizationProblem) for control will likely be worse! They probably need solution conditions lifted to DAE residual.
Maybe add explicit solver wrapper following new API. New API is well-organized & can likely wrap explicit+events and sundials CVODES/IDA relatively easily. SimuPy (explicit solver) version had problems for later orbital problems even though first orbital problem ~twice as fast (consistent with bmcage’s optimized example in discussion). Not sure if explicit issues for later orbital resolved by time-yielding
Modes definitely need if_else control branch instead of *float(bool) for explicit solver. Lifted DAE approach may be less important (although number of residuals may change…)
Use the built-in sensitivity method of IDAS/CVODES for the continuous portions, then SGM equations for discontinuities. May be able to minimize storage requirements/accuracy

## Slide 17: Gascon
GASP Advancement using Symbolics in CONdor
…Analysis and Supplemental modeling…
… Substitutable models? Solutions? Etc.
Demonstrate achievement of condor goals by giving two under-graduate summer interns 10 weeks to re-implement GASPy, which took a team of experienced engineers 2+ years to implement
Fastest path to solve EPFD’s coupled optimization problem

## Slide 18
Try removing clipping and using implicit_output's lower_bound to enforce positive solution
and/or as an optimization problem
ascent controller as optimization problem
Clean up trajectory? lol
Add CL alpha calculation (See Dahlia/Carl chat)
Add VROT calculation to statics
condor import settings for GasconAnalysis to make sure it is using the correct engine deck
refactor to use for-loop promotion pattern, make variable names more consistent
Aero form factors computation
Other GITHUB Gaspy todo
Propeller idle