## Slide 1
Datetime | Load
2023-02-03 10:00:00Z | 8.2
2023-02-03 10:15:00Z | 8.6
… | …
Windspeed | APX | E1C_AMI_A | …
3.2 | 48.0 | 0.0012 | 
3.8 | 48.0 | 0.0015 | 
… |  |  | 
Load 2days before | Load 15 mins before | Wind Energy | Dew-point | isWeekday | …
14.3 | 7.8 | 0.20 | 8.9 | 0 | 
14.6 | 8.2 | 0.23 | 9.1 | 0 | 
… |  |  |  |  | 
Load
Weather Forecasts
Market Prices
Typical Profiles
Derived Weather
Derived Renewable
Lagged Load
Target – y
External Predictors
Derived Features
Features - X
Input Backtest Pipeline
Calculates
Multiply for training horizons
Datetime (excl in fit) | Load | Windspeed | APX | E1C_AMI_A | … | Load 2days before | Load 15 mins before | Wind Energy | Dew-point | … | Horizon (excl. in fit)
2023-02-03 10:00:00Z | 8.2 | 3.2 | 48.0 | 0.0012 |  | 14.3 | 7.8 | 0.20 | 8.9 |  | 0.25
2023-02-03 10:00:00Z | 8.2 | 3.2 |  | 0.0012 |  | 14.3 |  | 0.20 | 8.9 |  | 47.0
2023-02-03 10:15:00Z | 8.6 | 3.8 | 48.0 | 0.0015 |  | 14.6 | 8.2 | 0.23 | 9.1 |  | 0.25
2023-02-03 10:15:00Z | 8.6 | 3.8 |  | 0.0015 |  | 14.6 |  | 0.23 | 9.1 |  | 47.0
… |  |  |  |  |  |  |  |  |  |  | 
1) OpenSTEF forecasts a timeseries with a known history; the Target. Typically this is the measured load on an asset.
Calendar Info
2) The Target is merged with External Predictors, such as Weather Forecasts.
3) Derived Features are calculated, such as the Lagged Target, weekday and the generation of a typical wind turbine
4) OpenSTEF trains a single model to predict the load at all lead times. This is performed by duplicating the training data for every training horizon (typically 15 minutes ahead and 47 hours ahead), and masking all features which are operationally not available at that training horizon. E.g. The day-ahead electricity price is known for a training horizon of 15 minutes, but not for 47 hours. This way, the model has increased predictive power for short lead times, while also able to make a sensible prediction at long lead times
model.fit
4) During Forecasting, the model predicts in a single shot all requested lead times, typically up to 48 hours ahead with a 15 minute resolution.
Wind-speed | APX | E1C_AMI_A | … | Load 2days before | Load 15 mins before | Wind Energy | Dew-point | …
4.2 | 52.0 | 0.0013 |  | 5.2 | 5.1 | 0.60 | 7.1 | 
4.4 | 52.0 | 0.0013 |  | 5.7 |  | 0.68 | 7.3 | 
8.8 |  | 0.0015 |  | 5.1 |  | 0.88 | 7.1 | 
model.predict
Datetime | Load Forecast
2023-02-04 07:00:00Z | 7.6
2023-02-04 07:15:00Z | 7.8
… | 
2023-02-05 06:45:00Z | 7.4
Datetime
2023-02-04 07:00:00Z
2023-02-04 07:15:00Z
…
2023-02-04 06:45:00Z
Forecast @ 2023-02-03 06:50:00Z

## Slide 2
Quantile Regression
←Realized
Forecast→
P98
P84
P50 = Forecast
P02
P16
Higher uncertainty for high values
Higher uncertainty for low values
Standard Deviation
Higher uncertainty
Lower uncertainty
Forecast + 2σ ≈ P98
Forecast + σ ≈ P84
Forecast = P50
Forecast - 2σ ≈ P02
Forecast - σ ≈ P16
A dedicated machine learning model is trained to predict each Percentile (e.g. P84) value seperately. The Percentile represents the chance that an observations lies below that value. Training a model for each percentile seperately is computationally expensive, but allows for complex interactions resulting in uncertainty to be captured.
Method: the pinball loss function is used during training, to generate an individual model for every percentile.
More information:
Probabilistic Forecasts: Pinball Loss Function | Towards Data Science
Implementation in OpenSTEF
No forecast is perfect. Therefore, it is valuable to provide a range of possible values instead of just one specific value. Different methods can be used to give a "band" of predictions, rather than a single point.
The following two methodologies are included in OpenSTEF.
Uncertainty can be approximated by calculating the standard deviation of the forecasting error. If the error is assumed to be normally distributed, Percentile values can be calculated. By grouping the standard deviation by for example the time of day, more and less certain moments can be distinguished. This method requires little computing time, but achieves a limited accuracy for typical energy profiles.
Method: The standard deviation of the forecasting error is calculated on a left-out-of-training validation set. This is grouped by a relevant parameter, such as the time of day.
More information: Small Data, Large Uncertainty | Towards Data Science
Implmentation in OpenSTEF
Estimating Uncertainty
model.predict
Datetime | Load Forecast | St dev | P02 | ... | P98
2023-02-04 07:00:00Z | 7.6 | 1.3 | 7.0 |  | 9.0
2023-02-04 07:15:00Z | 7.8 | 1.8 | 7.1 |  | 9.4
… |  |  |  |  | 
2023-02-05 06:45:00Z | 7.4 | 1.2 | 5.4 |  | 7.8
Notes on interpretation
A Percentile represents the chance an observation will exceed that value. For example, a P90 of 8 MW means that there is a 10% chance that at that moment the realization will exceed 8 MW
History vs Future; quantiles and standard deviations are represent past uncertainty. Structural breaks in the timeseries can cause future uncertainty to be inaccurately predicted. Retraining the model typically solves this.
Very high or very low quantiles are difficult to predict, since those span only few datapoints. Be skeptical of P>95 or P<05 values
Crossing percentiles; Since quantile regression trains seperate models for each percentile, P-lines can cross.
Forecast + 2σ ≈ P98
Forecast + σ ≈ P84
Forecast = P50
Forecast - 2σ ≈ P02
Forecast - σ ≈ P16
Given percentiles, the standard deviation can be approximated. For example: sigma = (p98-p50)/2 or sigma = (p84-p50). However, since errors typically are not normally distributed, these give different results. Expert knowledge on specific usecases is required to define a sensible strategy for this.

## Slide 3
Load
External Predictors
Weather forecasts
Derived Features
Windspeed
Radiation
Temperature
…
Market Prices
Day Ahead Electricity
…
Typical Profiles
Household with PV
Business
…
Derived Weather features
Derived Renewable
Global Tilt Irradiance
Dewpoint
…
Typical Solar Park
Typical Wind Turbine
Calendar
IsWeekday
IsHoliday
…
Target
Household
Lagged Load
Load two days before
Load 15 minutes before
…